## Slide 1: TwinCAT Connectivity

## Slide 2: TwinCAT Connectivity Big Picture
194/212/229
PC Hardware
TwinCAT 3
153/42/108
Connectivity
153/42/108
PLC
153/42/108
PLC
Safety
153/42/108
Motion
153/42/108
CCAT
Modules
153/42/108
Simulink®
Module
153/42/108
Measurement
and Analytics
153/42/108
Vision Runtime
153/42/108
HMI
153/42/108
CNC
153/42/108
Robotics Motion
153/42/108
IoT Communication
HTTPs
MQTT
153/42/108
Database Connection
153/42/108
TCP/IP
153/42/108
153/42/108
ADS
153/42/108
EtherCAT Automation Protocol
153/42/108
PROFINET, EtherNet/IP,
Modbus
153/42/108
M2M
153/42/108
MES / WES
153/42/108
HMI
153/42/108
MATLAB®
153/42/108
LabView®
Cloud Connectivity + Analytics
DB
ERP
RS232
RS485

## Slide 3: TwinCAT Connectivity IoT Functions
TF6730 IoT Communicator
Smartphone app
Incl. PLC Function Blocks
IoT product family overview
  Expose the underlying protocol(s):
    MQTT, OPC UA, REST, Web Sockets
    Flexible and customizable via PLC APIs, JSON/XML tooling
  Competitors are typically tightly coupled to an application or service
TF6701 IoT Communication
MQTT client connectivity
Real-time driver for the PLC
TF6720 IoT Data Agent
IoT gateway application
Standalone tool
TF6710 IoT Functions
Data Agent access
Real-time driver for the PLC
TF6760 IoT HTTP/REST
HTTP(S) client connectivity
Real-time driver for the PLC
TF6770 IoT WebSockets
WebSockets client
WebSockets server
Real-time driver for the PLC
TF6020 JSON Data Interface
Req/Res MQTT connectivity
ADS interface for PLC
TF6100 OPC UA
OPC UA connectivity
Client, Server, Gateway
TF6105 OPC UA Pub/Sub
OPC UA Pub/Sub connectivity
MQTT, UDP
MQTT, WSS,
HTTPS, OCPP,
OPC UA
Microsoft Azure
Thingspeak
TF6771 IoT OCPP
OCPP client connectivity
OCPP server connectivity
Real-time driver for the PLC
TwinCAT Cloud Engineering
MQTT, WSS,
HTTPS, OCPP,
OPC UA
MQTT, WSS,
HTTPS, OCPP,
OPC UA
Notes: We do have one out-of-the-box IoT solution with the communicator app
ADS discussion
JSON serialization discussion

## Slide 4: TwinCAT Connectivity MQTT
“A lightweight, publish-subscribe, machine to machine network protocol.”
Originally designed for remote sites with low-bandwidth or unreliable networks.
Why is MQTT ideal for IoT?
  Simple
    Pub/sub simplifies device communications and routing
    Supports multiple data formats
  Secure
    Supports TLS (certificate-based encryption)
  Performant

## Slide 5: TwinCAT Connectivity Traditional MES Communication Model
IT System
Networking
IP Address: 10.10.1.10
Protocol: ModbusTCP
Data Address: 432770
Data Format: 2x 16-bit words
Transaction
OT System
IP Address: 10.10.2.10
Protocol: Beckhoff ADS
Data Address: ‘PLC1.MAIN.eStatus’
Data Format: 1x 32-bit DINT
Transaction
To transact with each OT device, we need:
  Networking
    Security, firewall
    Address routing, NAT
  Application protocol driver
    Port numbers
    Device/node addressing
    Vendor software
  Data address and type information
    Type systems
    Byte packing, endianness
OT System
OT System
IP Address: …
Protocol: …
Data Address: …
Data Format: …
Transaction
Address Table
---------------
Machine1: 10.10.1.10
Machine2: 10.10.2.10
Machine#: 10.10.x.x
…

## Slide 6: TwinCAT Connectivity Broker Pub/Sub Model
IT System
To transact with each OT device, we need:
  Broker address
  Topic
Payloads can be binary or JSON (human-readable)
New components can simply connect to the broker and can begin publishing/subscribing
Topics created as needed, with user-defined names and “paths”:
Broker
OT System
Broker: 10.10.0.1
Topic: Machine/1/Status
Data: { ‘status’: ‘running’ }
Publish
OT System
Broker: 10.10.0.1
Topic: Machine/2/Status
Data: { ‘status’: ‘idle’ }
Publish
OT System
Subscribe
---------------
Broker: 10.10.0.1
Topic: Machine/#
Broker: 10.10.0.1
Topic: Machine/3/Status
Data: { ‘status’: ‘running’ }
Publish
Topic Subscription Messages Received
------------------- ---------------------------------
Machine/# All messages from all machines
Machine/1/# All messages from machine 1
Machine/1/Status Machine 1 status messages
Machine/+/Status Status messages from all machines

## Slide 7: TwinCAT Connectivity QoS and Retain
QoS (Quality of Service) – Means of guaranteeing message transfer to the broker, specified by the client
  Level 0: At most once
  Level 1: At least once
  Level 2: Exactly once
Retain – Mechanism for ensuring a subscriber received the message.
  A flag to inform the broker to hold onto the most recent “retain” message for a topic
  Any client subscribing to the topic, before or after the publish, will receive this message
Notes: QoS level 0
At this QoS level the receiver does not acknowledge receipt. The message is not sent a second time.
QoS level 1
At this QoS level the system guarantees that the message arrives at the receiver at least once, although the message may arrive more than once. The sender stores the message internally until it has received an acknowledgment from the receiver in the form of a PUBACK message. If the PUBACK message fails to arrive within a certain time, the message is resent.
QoS level 2
At this QoS level the system guarantees that the message arrives at the receiver no more than once. On the MQTT side this is realized through a handshake mechanism. QoS level 2 is the most secure level (from a message transfer perspective), but also the slowest. When a receiver receives a message with QoS level 2, it acknowledges the message with a PUBREC. The sender of the message remembers it internally until it has received a PUBCOMP. This additional handshake (compared with QoS 1) is important for avoiding duplicate transfer of the message. Once the sender of the message receives a PUBREC, it can discard the initial publish information, since it knows that the message was received once by the receiver. In other words, it remembers the PUBREC internally and sends a PUBREL. Once the receiver has received a PUBREL, it can discard the previously remembered states and respond with a PUBCOMP, and vice versa. Whenever a packet is lost, the respective communication device is responsible for resending the last message after a certain time.

## Slide 8: TwinCAT Connectivity Broker Scalability
Broker
Broker
Broker
Broker
Broker: cloud.broker.com
Topic: Site/1/Machine/2/Status
Data:
{
‘status’: ‘running’,
‘ppm’: 12.32,
‘uptime: ‘3:54:21’
…
}
Subscribe
Site 2
Site 1
Site 3
https://web.portal.com/site/1/machine/2/status
Broker-to-broker communications and cloud hosted brokers facilitate distributed, scalable connectivity
Formalize topic naming and hierarchy (“namespaces”) to organize site, machine and component level data
Web service can be introduced for external access
cloud.broker.com
2
3
1
Web server

## Slide 9: TwinCAT Connectivity Lab 1 – MQTT
Open MQTT Client of choice
Connect to iot.beckhoff.us:1883
  Validate connection by subscribing to ‘#’ to see all incoming messages (there will be tons)
  Unsubscribe from ‘#’ and subscribe to ‘nem_2024/#’
Reference and follow lab guide: [tinyurl]

## Slide 10: TwinCAT Connectivity HTTP/REST
Hyper Text Transfer Protocol (HTTP) is the ubiquitous language for web sites and services
Representational State Transfer (REST) is a set of architectural guidelines for web-based applications
  Describes how web clients and servers should interact at a high level
  “RESTful” APIs commonly use HTTP
Tons of technology relies on HTTP, not just websites:
  Native apps, mobile apps
  Package Managers
  Commercial systems; ERP, CMS, POS, etc.
  SaaS, PaaS systems
Very mature and comprehensive ecosystem of tooling
  Development tools, libraries
  Security, access control, encryption
Notes: Enterprise Resource Planning, content management system, point of sale

## Slide 11: TwinCAT Connectivity HTTP/REST
Hyper Text Transfer Protocol (HTTP) is the ubiquitous language for web sites and services
The most common HTTP methods are GET, POST, and PUT
  GET – Requests a resource from the server
  POST – Transfers data to the server
  PUT – Replaces or creates a resource on the server with the request payload
Notes: The POST method is used to request that the origin server accept the entity enclosed in the request as a new subordinate of the resource identified by the Request-URI in the Request-Line.
The PUT method requests that the enclosed entity be stored under the supplied Request-URI. If the Request-URI refers to an already existing resource, the enclosed entity SHOULD be considered as a modified version of the one residing on the origin server. If the Request-URI does not point to an existing resource, and that URI is capable of being defined as a new resource by the requesting user agent, the origin server can create the resource with that URI.

## Slide 12: TwinCAT Connectivity HTTP/REST
Representational State Transfer (REST) is a set of architectural guidelines for web-based applications
  Describes how web clients and servers should interact at a high level
  “RESTful” APIs commonly use HTTP
RESTful APIs follow 6 guiding principles
  Uniform Interface – Must be usable from different endpoints in a consistent manner
  Client-Server – User interface and data concerns are independent
  Stateless – Every client request must contain all information needed to process it
  Cacheable – Responses are labeled as cacheable or non-cacheable
  Layered System – Multilayered and hierarchical
  Code on Demand (Optional) – Client functionality can be extended by downloading code
Notes: Stateless – the server cannot take advantage of previously stored context
Cacheable – A client can cache server responses for future requests, but the info might be outdated.
Layered System – Each component cannot see beyond the layer it is interacting with
Code on Demand – Code can be executed in the form of applets or script

## Slide 13: TwinCAT Connectivity HTTP/REST Query Parameters
  Query parameters are used to specify resources from a server in a way which sorts/filters the resources.
  https://www.beckhoff-weather.com/forecast?city=verl
  https://www.beckhoff-weather.com - Domain
  /forecast - Path
  ?city=verl - Query parameter, where ‘?’ indicates the start of the query string

## Slide 14: TwinCAT Connectivity HTTP/REST – Exercises
Exercise 1: Web Browser
  Open your browser of choice
  Open developer tools (usually Ctrl + Shift + i)
  Open the ‘Network’ tab
  Load a web page – observe requests
    Markup, binary data (e.g. images), JavaScript, JSON – all retrieved via HTTP requests
Exercise 2: cURL, wget, Invoke-WebRequest
  Open a PowerShell terminal
  Use any one of the above commands
  Type in an endpoint, e.g. ‘httpbin.org/get’
Exercise 3 (optional): Postman or other tools
  Tons of HTTP-based API test tools out there
  Provide a nice GUI for viewing and editing requests/responses

## Slide 15: TwinCAT Connectivity Lab 2 – HTTP
Reference and follow lab guide: [tinyurl]
Web API
Encrypted
(HTTPS)
Authorized
Which protocol?
Is it secure?
Extra hardware
Extra software
<super secret recipe data>
Authorized
Encrypted
(HTTPS)
Not HTTP capable